## AHD-XM350-0239-32X32-V2_02 Interface Description

## Detailed Definition：

| Socket | Specific No. | Interface Description | Function |
| --- | --- | --- | --- |
| CN2 | 1 | CVBS | Video Out |
|  | 2 | GND | Ground |
|  | 3 | 12V | 12V DC input |
| CN1 | 1 | IRCUTA | IRCUT |
|  | 2 | IRCUTB |  |
| J1 | 1 | ADC1VIN | Red_CTRL |
|  | 2 | GND | Ground |
|  | 3 | NC | Undefined |
| J2 | 1 | ALARM_IN1 | White light CTRL |
|  | 2 | GND | Ground |
|  | 3 | 3.3V | 3.3V DC input |
|  | 4 | GND | Ground |
| J3 | 1 | GND | Ground |
|  | 2 | CVI | Switch to CVI by grounding |
|  | 3 | MODE_N-P | Red_CTRL |
|  | 4 | TVI | Switch to TVI by grounding |

# Text boxes

CN1  1 2

CN2   1 2 3

J2

4

3

2

1

J3   4 3 2 1

J1  3 2 1