IP Zoom Module Interface Instruction

| Interface | Pinout | Description | Function |
| --- | --- | --- | --- |
| P1 | 1 | ETHRX- | Ethernet,receive/send signal(-) |
|  | 2 | ETHRX+ | Ethernet,receive/send signal(+) |
|  | 3 | ETHTX- | Ethernet,receive/send signal(-) |
|  | 4 | ETHTX+ | Ethernet,receive/send signal(+) |
| P2 | 1 | DC_IN | DC power input,+9V--+12V |
|  | 2 | GND | Ground |
|  | 3 | RXD1 | RS-232，using RS485 protocol |
|  | 4 | TXD1 | RS-232，using RS485 protocol |
|  | 5 | RXD0 | RS-232, using VISCA protocol |
|  | 6 | TXD0 | RS-232, using VISCA protocol |
| P3 | 1 | GND | Ground |
|  | 2 | Reserve | Reserve |
|  | 3 | GND | Ground |
|  | 4 | AO_LINE | Audio Output |
|  | 5 | AI_LINE | Audio Input |